## Slide 1: Enhancing and Exploiting Contiguity for Fast Memory Virtualization
Chloe Alverti, Stratos Psomadakis, Vasileios karakostas, Jayneel Gandhi*, koNstANTINOS NIKAS, Georgios Goumas, Nectarios Kozyris
National technical university of Athens * VMware Research
Notes: Increase Fonts
Add logos

## Slide 2: Executive Summary
Problem: Address translation overheads in virtualized execution
Solution:
  SW: Contiguity-Aware paging Enhance the OS memory manager to support contiguous page allocations
  HW: Speculative Offset Address Translation (SpOT) Exploit the above generated contiguity to predict address translation
Results: Translation overheads from ~16% down to ~0.9% on average

## Slide 3: Outline
Background
SW: Contiguity-Aware paging
HW: Speculative Offset Address Translation (SpOT)
Evaluation
Conclusions

## Slide 4: 2D Address Translation in Virtualized Execution
Guest Virtual
Address
Guest Physical
Address
gVA
gPA
hPA
Host Physical
Address
Guest
Page Table
Nested
Page Table
1
2

## Slide 5: Nested Paging Overhead in x86
TLB
CR3
gVA
Memory Access
+ 5
+ 5
+ 5
+ 4
hPA
= 24
5
gVA hPA
Load gVA
HIT
MISS
Notes: 5 level in the middle
Make background a different color to make the thing to look better

## Slide 6: Nested Paging Overhead in x86
TLB
CR3
gVA
Memory Access
+ 5
+ 5
+ 5
+ 4
hPA
= 24
5
gVA hPA
Load gVA
HIT
MISS
Intel’s 5-Level Paging  brings this up to 35 Memory Accesses
Notes: 5 level in the middle
Make background a different color to make the thing to look better

## Slide 7: Prior Approaches: Mitigate Translation Overheads
Page Size
State of practice: Huge Pages
   HW budget (TLB),  OS support (THP)
  Significantly reduce but fail to eliminate overheads (~16.5%)
State of the art: Contiguous Mappings
  1 Translation Entry  multiple contiguously mapped pages
  Variable size  increased coverage
  Direct Segments [ISCA 13], Redundant Memory Mappings [ISCA 15], TLB Coalescing [MICRO12, HPCA 14, ISCA 17]
VA
PA
Notes: Change Range Translations name
Add citations

## Slide 8: Prior Approaches: Mitigate Translation Overheads
Page Size
State of practice: Huge Pages
   HW budget (TLB),  OS support (THP)
  Significantly reduce but fail to eliminate overheads (~16.5%)
State of the art: Contiguous Mappings
  1 Translation Entry  multiple contiguously mapped pages
  Variable size  increased coverage
  Direct Segments [ISCA 13], Redundant Memory Mappings [ISCA 15], TLB Coalescing [ISCA 17] ,
VA
PA
No dedicated OS allocation support and prior HW proposals are either too complex
or sacrifice performance potential in virtualized execution
Notes: Change Range Translations name
Add citations

## Slide 9: Our Goal
Efficient OS support for contiguous page mappings creation
  Preserve demand paging benefits
Efficient HW support to exploit the generated contiguity
  Particularly attractive to virtualized environments
Notes: Remove the picture
Reduce the text
Particularly attractive to 2D environments
Sub bullets

## Slide 10: Outline
Background
SW: Contiguity-Aware paging
HW: Speculative Offset Address Translation (SpOT)
Evaluation
Conclusions

## Slide 11: Demand Paging
Virtual Memory Areas (VMA)  malloc(), mmap(), etc.
malloc
VA
PA
VMA1
VMA2

## Slide 12: Demand Paging
VA
PA
VMA1
VMA2
Virtual Memory Areas (VMA)  malloc(), mmap(), etc.
Physical Pages  OS on demand allocation (access)
Page Fault
Notes: Again make background grey
Keep everything either black or bad things red

## Slide 13: Demand Paging
Page Fault
VA
PA
VMA1
VMA2
Virtual Memory Areas (VMA)  malloc(), mmap(), etc.
Physical Pages  OS on demand allocation (access)
OS random physical page allocations inhibit the creation of contiguous mappings
Notes: Again make background grey
Keep everything either black or bad things red

## Slide 14: Prior Work: OS support for contiguous mappings
 | Direct Segment [ISCA 13] |  | 
Allocation On Demand |  |  | 
Instant Creation of Contiguous Mappings |  |  | 
Multiple Mappings |  |  | 
Paging Support |  |  | 
Resilient to External Fragmentation |  |  | 
No Page Migrations |  |  | 
VA
PA
Segment
Segment





Application spawn  segment pre-allocation


## Slide 15: Prior Work: OS support for contiguous mappings
 | Direct Segment [ISCA 13] | Eager Paging [ISCA 15] | 
Allocation On Demand |  |  | 
Instant Creation of Contiguous Mappings |  |  | 
Multiple Mappings |  |  | 
Paging Support |  |  | 
Resilient to External Fragmentation |  |  | 
No Page Migrations |  |  | 
VA
PA
VMA1
VMA2






malloc()  VMA pre-allocation







## Slide 16: Prior Work: OS support for contiguous mappings
 | Direct Segment [ISCA 13] | Eager Paging [ISCA 15] | Ranger [ISCA 19]
Allocation On Demand |  |  | 
Instant Creation of Contiguous Mappings |  |  | 
Multiple Mappings |  |  | 
Paging Support |  |  | 
Resilient to External Fragmentation |  |  | 
No Page Migrations |  |  | 

VA
PA
VMA1
VMA2
VA
PA
VMA1
VMA2





Post-allocation asynchronous migrations













## Slide 17: Our Approach: Contiguity Aware (CA) Paging
 | Direct Segment [ISCA 13] | Eager Paging [ISCA 15] | Ranger [ISCA 19] | CA Paging
Allocation On Demand |  |  |  | 
Instant Creation of Contiguous Mappings |  |  |  | 
Multiple Mappings |  |  |  | 
Paging Support |  |  |  | 
Resilient to External Fragmentation |  |  |  | 
No Page Migrations |  |  |  | 
VA
PA
VMA2
VMA1
























Notes: Green  find a nice green
Reduce lines

## Slide 18: Contiguity Aware Paging: Basic Mechanism
VA
PA
VMA1
VMA2
Buddy Allocator Aligned Free Block Lists
……..
2M
4M
4K
8K
struct VMA {
…
}
Demand Paging  arbitrary page allocation
Fault

## Slide 19: Contiguity Aware Paging: Basic Mechanism
VA
PA
VMA1
VMA2
Buddy Allocator Aligned Free Block Lists
……..
2M
4M
4K
8K
struct VMA {
…
}
CA Paging  target page allocation
Fault
Target
Free?
Offset
Offset; // VA-PA

## Slide 20: Contiguity Aware Paging: Basic Mechanism
VA
PA
VMA1
VMA2
Buddy Allocator Aligned Free Block Lists
……..
2M
4M
4K
8K
struct VMA {
…
}
CA Paging  target page allocation
Fault
Offset
Offset; // VA-PA

## Slide 21: Contiguity Aware Paging: Basic Mechanism
VA
PA
VMA1
VMA2
Buddy Allocator Aligned Free Block Lists
……..
2M
4M
4K
8K
struct VMA {
…
}
CA Paging  target page allocation
Fault
Offset
Offset; // VA-PA
CA Paging extends gradually contiguous mappings across faults

## Slide 22: Contiguity Aware Paging: First Fault
VA
VMA1
VMA2
PA
Occupied
PA1
PA2
PA3
PA4
The first VMA fault sets the Offset
Random placement may interfere with fragmented parts of the memory

## Slide 23: Contiguity Aware Paging: First Fault
PA1,Size
Contiguity Map
VA
VMA1
VMA2
PA2,Size
PA3,Size
PA4,Size
PA
Occupied
PA1
PA2
PA3
PA4
Tracks unaligned, unlimited, larger than 4M contiguity
Buddy Allocator  aligned contiguity up to 4M

## Slide 24: Contiguity Aware Paging: First Fault
PA1,Size
Contiguity Map
VA
VMA1
VMA2
PA2,Size
PA3,Size
PA4,Size
PA
Occupied
PA1
PA2
PA3
PA4
Fault
Search contiguity map by VMA size

## Slide 25: Contiguity Aware Paging: First Fault
PA1,Size
Contiguity Map
VA
VMA1
VMA2
PA2,Size
PA3,Size
PA4,Size
PA
Occupied
PA1
PA2
PA3
PA4
Fault
No block reservation or pre-allocation

## Slide 26: Contiguity Aware Paging: Next Fit
PA1,Size
Contiguity Map
VA
VMA1
VMA2
PA2,Size
PA3,Size
PA4,Size
PA
Occupied
PA1
PA2
PA3
PA4
Next fit
Next fit placement to avoid competition

## Slide 27: Contiguity Aware Paging: Next Fit
PA1,Size
Contiguity Map
VA
VMA1
VMA2
PA2,Size
PA3,Size
PA4,Size
PA
Occupied
PA1
PA2
PA3
PA4
Next fit
Next fit placement to avoid competition

## Slide 28: Contiguity Aware Paging: Next Fit
PA1,Size
Contiguity Map
VA
VMA1
VMA2
PA2,Size
PA3,Size
PA4,Size
PA
Occupied
PA1
PA2
PA3
PA4
Next fit
Next fit placement to avoid competition

## Slide 29: How it works in a 2D environment
gVA
gPA
VMA
hPA
Guest CA paging (page fault)
Host CA paging
(nested fault)
CA paging is applied independently in each dimension without coordination, following nested paging philosophy
Notes: Represent the end-to-end mapping (show the splitted ranges)
Mismatches in gVAgPA and gPA hPA ranges may appear (details in the paper)
Fits with nested paging philosophy
Remove passive voice

## Slide 30
Background
SW: Contiguity-Aware paging
HW: Speculative Offset Address Translation (SpOT)
Evaluation
Conclusions
Outline
Notes: Transition

## Slide 31
Prior Work: HW translation schemes
Deterministic: explicit tracking of the mappings boundaries
…
VA
PA
No complex Architectural Support |  |  | 
No Alignment Restrictions |  |  | 
Multiple Mappings Support |  |  | 

## Slide 32
…
VA
PA
Segment
Segment
(BASE,LIMIT)  OFFSET
Registers
Base
Limit
Offset
Deterministic: explicit tracking of the mappings boundaries
 | Direct Segment [ISCA 13] |  | 
No complex Architectural Support |  |  | 
No Alignment Restrictions |  |  | 
Multiple Mappings Support |  |  | 



Prior Work: HW translation schemes

## Slide 33
VA
PA
Base1
Limit1
Offset1
Base2
Limit2
Offset2
Range TLB
(BASE1,LIMIT1)  OFFSET1
(BASE2,LIMIT2)  OFFSET2
(BASEn,LIMITn)  OFFSETn
…
CR-RT
Range Table
Deterministic: explicit tracking of the mappings boundaries
 | Direct Segment [ISCA 13] | RMM [ISCA 15] | 
No complex Architectural Support |  |  | 
No Alignment Restrictions |  |  | 
Multiple Mappings Support |  |  | 






Prior Work: HW translation schemes
Notes: Say the things on the black boxes !

## Slide 34
VA
PA
V1
V3
Commodity TLB
V1,P1
V3,P3
P1
P3
+4
+3
Deterministic: explicit tracking of the mappings boundaries
 | Direct Segment [ISCA 13] | RMM [ISCA 15] | TLB Coalescing [ISCA 17]
No complex Architectural Support |  |  | 
No Alignment Restrictions |  |  | 
Multiple Mappings Support |  |  | 









Prior Work: HW translation schemes

## Slide 35
VA
PA
V1
V3
Commodity TLB
V1,P1,+2
V2,P2,+2
V3,P3,+3
P1
P3
V2
P2
Deterministic: explicit tracking of the mappings boundaries
 | Direct Segment [ISCA 13] | RMM [ISCA 15] | TLB Coalescing [ISCA 17]
No complex Architectural Support |  |  | 
No Alignment Restrictions |  |  | 
Multiple Mappings Support |  |  | 









Prior Work: HW translation schemes

## Slide 36
Challenging 2D environment
gVA
gPA
hPA
2D Offset1
2D Offset2
gBase1
gLimit1
gBase2
gLimit2
gOffset1
gOffset2
hBase1
hLimit1
hBase2
hLimit2
hOffset1
hOffset2
Notes: Base Limit Increase Font
Make Offsets horizontal
Consider Having two different ranges

## Slide 37
gVA
gPA
hPA
2D Offset1
2D Offset2
gBase1
gLimit1
gBase2
gLimit2
gOffset1
gOffset2
hBase1
hLimit1
hBase2
hLimit2
hOffset1
hOffset2
Explicit tracking sacrifices performance or increases HW complexity
Challenging 2D environment
Notes: Base Limit Increase Font
Make Offsets horizontal
Consider Having two different ranges

## Slide 38
gVA
gPA
hPA
2D Offset1
2D Offset2
gBase1
gLimit1
gBase2
gLimit2
gOffset1
gOffset2
hBase1
hLimit1
hBase2
hLimit2
hOffset1
hOffset2
Speculative Offset Address Translation (SpOT)
Notes: Base Limit Increase Font
Make Offsets horizontal
Consider Having two different ranges

## Slide 39
gVA
gPA
hPA
2D Offset1
2D Offset2
Speculative Offset Address Translation (SpOT)
Speculate the existence of contiguous mappings Predict address translations
Notes: Base Limit Increase Font
Make Offsets horizontal
Consider Having two different ranges

## Slide 40
Speculative Offset Address Translation (SpOT)
Small prediction table
On the L2 TLB miss path
Stores 2D Offsets calculated on the fly
PC-indexed, set-associative
…
SpOT
PC1 Offset1
PCn Offsetn
PC
Notes: Color Up Spot  keep this on further
Make the struct look better
PC indexed at the micro-architectural level xwristo bullet

## Slide 41
gVA
gPA
hPA
Execute
Speculative Offset Address Translation (SpOT)

## Slide 42
Execute
Speculative Offset Address Translation (SpOT)
PC1  TLB miss
TLB miss
L2 TLB
gVA1
MISS
gVA1
gVA
gPA
hPA

## Slide 43
Execute
Speculative Offset Address Translation (SpOT)
PC1  TLB miss
TLB miss
L2 TLB
gVA1
gVA1
…
SpOT
PC1
Nested walk
MISS
Stall
Nested Page Walk
gVA
gPA
hPA

## Slide 44
Execute
Speculative Offset Address Translation (SpOT)
PC1  TLB miss
TLB miss
L2 TLB
gVA1
gVA1
…
SpOT
PC1
Nested walk
Stall
Nested Page Walk
update
PC1 Offset1
hPA1
Offset1
Execute
hPA1
gVA
gPA
hPA

## Slide 45
Execute
Speculative Offset Address Translation (SpOT)
PC1  TLB miss
TLB miss
L2 TLB
gVA2
gVA2
…
SpOT
PC1
Nested walk
PC1 Offset1
Spec hPA2
HIT
Spec Execute
Nested Page Walk
Spec hPA2 (gVA2 – Offset1)
gVA
gPA
hPA

## Slide 46
Execute
Speculative Offset Address Translation (SpOT)
PC1  TLB miss
TLB miss
L2 TLB
gVA2
gVA2
…
SpOT
PC1
Nested walk
PC1 Offset1
hPA2
Spec hPA2 (gVA2 – Offset1)
Spec Execute
Nested Page Walk
hPA2
?
Verify
gVA
gPA
hPA

## Slide 47
Execute
Speculative Offset Address Translation (SpOT)
PC1  TLB miss
TLB miss
L2 TLB
gVA2
gVA2
…
SpOT
PC1
Nested walk
PC1 Offset1
hPA2
Spec hPA2 (gVA2 – Offset1)
Spec Execute
Nested Page Walk
hPA2

Execute
gVA
gPA
hPA

## Slide 48
Execute
Speculative Offset Address Translation (SpOT)
PC1  TLB miss
TLB miss
L2 TLB
gVA2
gVA2
…
SpOT
PC1
Nested walk
PC1 Ofsset1
hPA2
Spec hPA2 (gVA2 – Offset1)
Spec Execute
Nested Page Walk
hPA2

Execute
gVA
gPA
hPA
SpOT hides nested page walk latency with speculative execution

## Slide 49
Execute
Speculative Offset Address Translation (SpOT)
TLB miss
L2 TLB
gVA3
…
SpOT
PC1
Nested walk
PC1 Offset1
hPA3
Spec hPA3 (gVA2 – Offset1)
Spec Execute
Nested Page Walk
hPA3

Execute
Penalty
gVA
gPA
hPA

## Slide 50
Execute
Speculative Offset Address Translation (SpOT)
TLB miss
L2 TLB
gVA3
…
SpOT
PC1
Nested walk
PC1 Offset1
hPA3
Spec Execute
Nested Page Walk
hPA3

Execute
Penalty
update
Mitigation techniques for Spectre/Meltdown [MICRO 18] address SpOT’s vulnerabilities (details in the paper)
gVA
gPA
hPA

## Slide 51
Background
SW: Contiguity-Aware paging
HW: Speculative Offset Address Translation (SpOT)
Evaluation
Conclusions
Outline

## Slide 52
Measure cost on page walks on real hardware
  Intel 2-socket 20-core Broadwell with 256GB memory
  1536-entry L2 TLB 6-way associative for 4KB/2M pages
Prototype CA Paging in Linux v4.19
  Linux pagemap  contiguity results
  https://github.com/cslab-ntua/contiguity-isca2020
  BadgerTrap [CAN 14]  online analysis of TLB misses and HW emulation
Linear model to predict performance
Workloads
  Big-memory workloads, machine learning, HPC
Methodology
Notes: citation

## Slide 53
Contiguity Results
32 Largest Mappings Coverage
Chart: 
| Hog-0 | Hog-20 | Hog-30 | Hog-40 | Hog-50
Ideal Paging | 100 | 100 | 100 | 99.8948 | 95.3039
THP | 4.4684 | 10.2009 | 6.0126 | 4.7742 | 3.5194
Eager Paging | 99.99 | 83.1634 | 72.2092 | 67.2578 | 61.844
Ranger | 87.471 | 92.4101 | 90.7203 | 93.1061 | 96.5263
CA paging | 98.9715 | 99.9925 | 99.724 | 98.3427 | 94.6236
X Ideal Paging
THP
Eager Paging [ISCA 15]
Ranger [ISCA 19]
CA paging
128 Largest Mappings Coverage
Chart: % Memory Footprint
| Hog-0 | Hog-20 | Hog-30 | Hog-40 | Hog-50
Ideal Paging | 100 | 74.5631 | 68.8211 | 60.7392 | 53.9949
THP | 1.9973 | 4.5878 | 2.5506 | 2.0762 | 1.4141
Eager paging | 99.99 | 43.4303 | 32.9983 | 31.6076 | 27.35
Ranger | 86.8353 | 75.3732 | 78.0119 | 80.1518 | 83.3979
CA paging | 98.6105 | 70.1416 | 67.0419 | 59.7265 | 54.1696
Notes: Add slide with virtualization results

## Slide 54
Contiguity Results
32 Largest Mappings Coverage
Chart: 
| Hog-0 | Hog-20 | Hog-30 | Hog-40 | Hog-50
Ideal Paging | 100 | 100 | 100 | 99.8948 | 95.3039
THP | 4.4684 | 10.2009 | 6.0126 | 4.7742 | 3.5194
Eager Paging | 99.99 | 83.1634 | 72.2092 | 67.2578 | 61.844
Ranger | 87.471 | 92.4101 | 90.7203 | 93.1061 | 96.5263
CA paging | 98.9715 | 99.9925 | 99.724 | 98.3427 | 94.6236
X Ideal Paging
THP
Eager Paging [ISCA 15]
Ranger [ISCA 19]
CA paging
128 Largest Mappings Coverage
Chart: % Memory Footprint
| Hog-0 | Hog-20 | Hog-30 | Hog-40 | Hog-50
Ideal Paging | 100 | 74.5631 | 68.8211 | 60.7392 | 53.9949
THP | 1.9973 | 4.5878 | 2.5506 | 2.0762 | 1.4141
CA paging | 98.6105 | 70.1416 | 67.0419 | 59.7265 | 54.1696
Eager paging | 99.99 | 43.4303 | 32.9983 | 31.6076 | 27.35
Ranger | 86.8353 | 75.3732 | 78.0119 | 80.1518 | 83.3979
Contiguity Aware Paging outperforms pre-allocation and performs similar/better to post-migrations for 128 mappings
Notes: Add slide with virtualization results

## Slide 55
Migration Pitfalls
Chart: Normalized execution
| Xbench | Geomean
THP | 1 | 1
Eager | 0.999 | 1.0013
Ranger | 1.0885 | 1.0355
CA paging | 1.0002 | 1.0027
Performance Overhead
Contiguity Generation Delay
Chart: Time (sec)
Eager | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9
CA Paging | 98.23 | 99.93 | 99.93 | 99.93 | 99.93 | 99.94 | 99.94 | 99.94 | 99.94 | 99.92 | 99.96 | 99.98 | 99.98 | 99.99 | 99.99 | 99.99 | 99.99 | 99.99 | 99.99 | 99.99 | 99.99
Ranger | 31.58 | 4.93 | 99.97 | 99.97 | 99.97 | 11.19 | 73.94 | 97.6 | 86.02 | 28.39 | 27.14 | 86.59 | 91.11 | 91.11 | 91.11 | 91.11 | 91.11 | 91.11 | 91.11 | 91.11 | 91.11
Notes: Take away messages
Re-arrange what shown

## Slide 56
Migration Pitfalls
Chart: Normalized execution
| Xbench | Geomean
THP | 1 | 1
Eager | 0.999 | 1.0013
Ranger | 1.0885 | 1.0355
CA paging | 1.0002 | 1.0027
Performance Overhead
Contiguity Generation Delay
Chart: Time (sec)
Eager | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9 | 99.9
CA Paging | 98.23 | 99.93 | 99.93 | 99.93 | 99.93 | 99.94 | 99.94 | 99.94 | 99.94 | 99.92 | 99.96 | 99.98 | 99.98 | 99.99 | 99.99 | 99.99 | 99.99 | 99.99 | 99.99 | 99.99 | 99.99
Ranger | 31.58 | 4.93 | 99.97 | 99.97 | 99.97 | 11.19 | 73.94 | 97.6 | 86.02 | 28.39 | 27.14 | 86.59 | 91.11 | 91.11 | 91.11 | 91.11 | 91.11 | 91.11 | 91.11 | 91.11 | 91.11
CA paging works on the allocation path avoiding any delays in contiguity generation and adds no overhead
Notes: Take away messages
Re-arrange what shown

## Slide 57
Performance Results
Compare SpOT + CA paging with:
  4K/THP paging
  Virtualized RMM (vRMM) [ISCA 15] + CA paging
  Direct Segments (DS) [MICRO 14]
    In Dual Mode (maximum performance)
    Their own SW reservation component

## Slide 58
Performance Results
Chart: Execution Overhead (%)
| 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | SVM | XSBench | Geomean
 | 76.041 | 222.8167 | 13.3696 | 28.3794 | 1.1352 | 0.6 | 2.972 | 52.8611 | 165.2826 | 6.6767 | 14.8926 | 0.014893 | 0.0001 | 0.69034 | 66.1929 | 132.1869 | 7.121 | 16.4527 | 0.089726 | 0.0044777 | 0.84961
76.04%
52.86%
66.19%

## Slide 59
Performance Results
Chart: Execution Overhead (%)
| 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | SVM | XSBench | Geomean
 | 76.041 | 222.8167 | 13.3696 | 28.3794 | 1.1352 | 0.6 | 2.972 | 52.8611 | 165.2826 | 6.6767 | 14.8926 | 0.014893 | 0.0001 | 0.69034 | 66.1929 | 132.1869 | 7.121 | 16.4527 | 0.089726 | 0.0044777 | 0.84961
76.04%
52.86%
66.19%
222%
165%
132%

## Slide 60
Performance Results
Chart: Execution Overhead (%)
| 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | SVM | XSBench | Geomean
 | 76.041 | 222.8167 | 13.3696 | 28.3794 | 1.1352 | 0.6 | 2.972 | 52.8611 | 165.2826 | 6.6767 | 14.8926 | 0.014893 | 0.0001 | 0.69034 | 66.1929 | 132.1869 | 7.121 | 16.4527 | 0.089726 | 0.0044777 | 0.84961
76.04%
52.86%
66.19%
222%
165%
132%

## Slide 61
Performance Results
Chart: Execution Overhead (%)
| 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | SVM | XSBench | Geomean
 | 76.041 | 222.8167 | 13.3696 | 28.3794 | 1.1352 | 0.6 | 2.972 | 52.8611 | 165.2826 | 6.6767 | 14.8926 | 0.014893 | 0.0001 | 0.69034 | 66.1929 | 132.1869 | 7.121 | 16.4527 | 0.089726 | 0.0044777 | 0.84961
76.04%
52.86%
66.19%
222%
165%
132%

## Slide 62
Performance Results
Chart: Execution Overhead (%)
| 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | SVM | XSBench | Geomean
 | 76.041 | 222.8167 | 13.3696 | 28.3794 | 1.1352 | 0.6 | 2.972 | 52.8611 | 165.2826 | 6.6767 | 14.8926 | 0.014893 | 0.0001 | 0.69034 | 66.1929 | 132.1869 | 7.121 | 16.4527 | 0.089726 | 0.0044777 | 0.84961
76.04%
52.86%
66.19%
222%
165%
132%

## Slide 63
Performance Results
Chart: Execution Overhead (%)
| 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | 4K | 4K+4K | THP | THP+THP | vRMM | DS | SPOT | SVM | XSBench | Geomean
 | 76.041 | 222.8167 | 13.3696 | 28.3794 | 1.1352 | 0.6 | 2.972 | 52.8611 | 165.2826 | 6.6767 | 14.8926 | 0.014893 | 0.0001 | 0.69034 | 66.1929 | 132.1869 | 7.121 | 16.4527 | 0.089726 | 0.0044777 | 0.84961
76.04%
52.86%
66.19%
222%
165%
132%
SpOT has comparable performance (<1%) to deterministic vRMM
while avoiding all the architectural complexity and to DS while avoiding the rigid SW support that it requires

## Slide 64: Conclusions
Problem: Address translation overhead in virtualized execution
Solution:
  SW: Contiguity-Aware paging
    OS contiguous page allocations on demand
    Native and virtualized environments
    Boosts the performance of any contiguous page mapping translation scheme
    https://github.com/cslab-ntua/contiguity-isca2020
  HW: Speculative Offset Address Translation (SpOT)
    Exploit the SW generated contiguity to predict translations
    Native and virtualized environments
Results: 2D Translation overhead from ~16% down to ~0.9% on average
Thank you!! 